## Slide 1: Indoor Localization Robot

## Slide 2: Introduction 00

## Slide 4: Web Application and Server 01

## Slide 5: Why Web Application ?
Managing and controlling robotic tasks through an intuitive web interface.

## Slide 6: Structure
Running the dashboard and send data reliably to the robot using ROS scripts.
Seamless interaction with robot and monitor performance.
A robust architecture, integrating databases and server-side logic to handle real-time communication.
Server
Back-end
Front-end

## Slide 7: Technology Stack

## Slide 8: Main Features
Flexibility in Adding Robots.
Creating Maps/Paths.
Creating and assigning tasks to robots.
Control robots with real-time data visualization.

## Slide 9: Hardware 02

## Slide 10: Guiding principles Mission Vision
In the end of the project, the infrastructure is designed to be:
Sourced locally.
Modular.
Open-Source.
To be able to provide a solid hardware infrastructure with relative ease.

## Slide 11: Robot Infra-structure:

## Slide 12: Power Board:
Multiple Outputs for Power Distribution.
5V conversion, for powering the used SBC.
Reverse Polarity and Overcurrent Protection.

## Slide 13: Auxiliary Boards:
Sensors Board.
Motion Board.
Actuators’ Board.

## Slide 14: Battery Management System
Protection Features:
Monitoring Features:
Overvoltage
Undervoltage
Overcurrent
Short Circuit.
Voltage of each module.
Total Current of the pack
Temperature.

## Slide 15: Visible Light Communication [VLC]
Transmitter
Receiver
A code is assigned to each region.
Controlled by a 220VAC LED
Each Bit maps to a certain received intensity.
BPW34 Micro solar cell
Transimpedance Amplifier.
Voltage Amplifier.
Decision making.

## Slide 16: Embedded 03
Sensing and Control

## Slide 17: Meccanum Wheels
Enable omnidirectional movement.

## Slide 18: Used Sensors
Ultrasonic sensor
IMU : MPU6050

## Slide 19: Sensors Board ROS Communication between Robot and Server
Motors Board

## Slide 20: STM32 Microcontroller Key Benefit Why STM32?
Balances performance and cost for diverse device integration.
Designed for high-performance yet low-cost applications.

## Slide 21: Thank You